## Slide 1: West Chicago FY 27 Water/Sewer Workshop
Water and Sewer FUNDS

## Slide 2: Fund Background

## Slide 3: Water Infrastructure at a glance
~2,500 Valves, ~2,000 FHs & ~7,100 water meters & services
~797 Lead Service Lines (LSL)
2 Booster Stations (Bishop St & Helena Dr) including one 500,000 Gallons Above Ground Storage at each location
5 Deep Sandstone Wells (~1,390 feet)
~147 miles of distribution network (includes ~8 miles of raw watermain)
9 MG Water Treatment Plant
4 Shallow Silurian Dolomite Wells (~325 feet)
2 Elevated Water Towers - Hawthorne Lane (500,000 Gallons) & Fremont St (250,000 Gallons)

## Slide 4: Sewer Infrastructure at a glance
~106 miles of sanitary collection system
7.4 MG Regional WCWWA WWTP
13 Sanitary Lift Stations
~1,500 Sanitary Manholes
~6,500 sanitary services

## Slide 5: Aging & Inadequate Infrastructure
35% of the water distribution pipes are over 50 years old (~51.4 miles)
Wastewater Treatment Plant is 43 years old
Oldest water meters are ~16 years old; typical life expectancy of ~15-20 years
Storage Shortfall: 1.75 MG available vs. 4.5 MG recommended in 2011 Study
27% of the water distribution pipes are undersized (<6"), limiting flow and fire protection (~37.5 miles)

## Slide 6: Aging & Inadequate Infrastructure
Hawthorne Tower (1967) & Fremont Tower (1959)
9 Wells, average age 37.3 years
13 Sanitary Lift Stations, average age 38.2 years
Water Treatment Plant-21 years old

## Slide 7: Revenue & Expenses

## Slide 8: FY 27 – 31 Water Estimated Revenue vs. Expenses
Revenues*
Water Service Charges - $46,368,600
IEPA SRF Loan - $20,832,600
Grants - $240,300
Total = $67,441,500
Expenses
Operations (Distribution) - $21,859,120
Operations (Production)- $14,571,245
Capital (Distribution)-$33,093,400**
Capital (Production)- $3,572,500
Transfers Out - $1,071,500
Total = $74,167,765
Revenues:
Expenses:
Total =
$67,441,500
$74,167,765
-$6,726,265
*Pre-planned 2027 and 2028 rate increases not included
** Includes Debt Service for LSLR ($1,292,700) & 1.5 MG Water Tower ($1,545,300)

## Slide 9: FY 27 – 31 Water Estimated Revenue vs. Expenses
Chart: Revenue vs Expenses
| 2027 | 2028 | 2029 | 2030 | 2031
Revenue | 17801200 | 21325400 | 9272800 | 9582800 | 9459300
Expenses | 18655065 | 21285300 | 9143700 | 11849300 | 13234400

## Slide 10: FY 27 – 31 Estimated Sewer Revenue vs. Expenses
Revenue*
Sewer Charges - $40,808,300
Grants - $210,100
Transfers In - $1,800,000**
Total = $42,818,400
expenses
Operations (Sewer) - $39,398,105
Capital (Sewer) - $12,324,300
Transfers Out - $131,700
Total = $51,854,105
Revenues:
Expenses:
Total =
$42,818,400
$51,854,105
-$9,035,705
*Pre-planned 2027 and 2028 rate increases not included
** Includes 50% of the 0.25% HRST increase (effective 1/1/27) from 2027-2029

## Slide 11: FY 27 – 31 Estimated Sewer Revenue vs. Expenses
Chart: Revenue vs. Expenses
| 2027 | 2028 | 2029 | 2030 | 2031
Revenue | 8725000 | 8741000 | 8760800 | 8266600 | 8325000
Expenses | 8453305 | 8104600 | 8787000 | 15966200 | 10543000

## Slide 12: Water CIP Program
Five Year outlook

## Slide 13: Project Determination
Grant Funding Deadlines
Pavement Reconstruction/Resurfacing
Sanitary Sewer Evaluation Survey
Watermain Break History
Age of Underground Infrastructure
Public Safety: LSLR
Unfunded Mandates: LSLR, Phosphorus Limits, etc.
2026 WWTP Condition Assessment (~$21 Million in CIP between 2027-36)
2024 WTP Condition Assessment Study (~$20.6 Million in CIP over 20-years starting in 2025)

## Slide 14: 5 YR Water-Sewer Capital Improvement Program
$2.41 Million – Well Houses
$16.62 Million* – Distribution System
$14.06 Million** - Water Storage
$3.57 Million – Water Treatment Plant
$12.32 Million – Sanitary Collection System
*12.5M - ~797 LSLR
**11.4M - 1.5 MG Elevated Tower

## Slide 15: Watermain Break History 2007-2022
70% of the breaks between 2007-2022 occurred on watermains with 50+ years of age
Since October 2022, approximately 125 watermain breaks have occurred (~31/year)
2022 Water Model study recommends City to replace 1.50 miles/year (~8,000 feet) - ~100-year replacement cycle
FY 2027-31, projected replacement is about 0.55 miles/year( ~2,900 feet) - ~267-year replacement cycle

## Slide 16: Rate Timeline

## Slide 17: West Chicago Historic Rates
Ordinance No. | Date Passed | Date Effective | Water Rate | Sewer (Residential) | Sewer (Commercial)
05-O-0009 | 5/1/2006 | 5/1/2006 | $2.90* ($3.88) | $2.68* ($3.58) | N/A
07-O-0019 | 7/1/2007 | 7/1/2007 | $2.90* ($3.88) | $2.90* ($3.88) | $3.06* ($4.09)
08-O-0006 | 7/1/2008 | 7/1/2008 | $2.90* ($3.88) | $3.50* ($4.68) | $3.66* ($4.89)
 | 7/1/2008 | 7/1/2009 | $2.90* ($3.88) | $4.20* ($5.61) | $4.36* ($5.82)
12-O-0010** | 4/11/2012 | 4/11/2012 | $3.88 | $5.61 | $5.82
19-O-0018 | 5/20/2019 & 5/20/2020*** | 7/1/2022 | $5.00 ($3.88 until 7/1/2022) | $7.00 ($5.61 until 7/1/2022) | $7.30 ($5.82 until 7/1/2022)
22-O-0036 | 12/5/2022 | 7/1/2023 | $9.00 | $10.00 | $10.30
23-O-0025 | 9/5/23 | 1/1/25 | $9.45 | $10.50 | $10.82
23-O-0025 | 9/5/23 | 1/1/26 | $9.90 | $11.00 | $11.34
*rates are per 100 cubic feet . **rates were switched to per 1,000 gallons (100 cubic feet = 748.5 gallons)
***Only rates effective 5/20/2020 were implemented on 7/1/2022 due to the pandemic

## Slide 18: Rate Comparison (Avg $10.86/$6.96)
Municipality | Approx. Population | Approx. Area (Square Miles) | Water Rates (1,000 Gallons) | Sewer Rates (1,000 Gallons)
West Chicago | 25,600 | 15 | $9.90 | $11.00
Downers Grove | 49,400 | 15 | $11.24 | $3.65*
Lombard | 43,300 | 10 | $11.40 | $7.74*
Addison | 34,800 | 10 | $11.58 | $8.47
Woodridge | 33,200 | 10 | $11.74 | $6.47*
Elmhurst | 45,000 | 10 | $14.82 | $11.45
Wheaton | 52,300 | 11 | $8.44 | $7.90*
Glen Ellyn | 28,000 | 7 | $10.50 | $7.57*
Westmont | 23,600 | 5 | $12.36 | $3.65*
Lisle | 22,900 | 7 | $8.04 | $6.24*
Villa Park | 21,400 | 5 | $10.54 | $3.85*
Darien | 21,500 | 6 | $9.75 | $5.57*
*served wholly/partially by various sanitary districts

## Slide 19: Rate Comparison – Continued ($9.12/$8.38)
Municipality | Approx. Population | Approx. Area (Square Miles) | Water Rates (1,000 Gallons) | Sewer Rates (1,000 Gallons)
West Chicago | 25,600 | 15 | $9.90 | $11.00
Aurora | 175,700 | 45 | $10.29** | $11.07*
Batavia | 26,100 | 11 | $5.79 | $8.66*
St. Charles | 32,400 | 14 | $11.70 | $8.83
Montgomery | 22,900 | 10 | $8.93** | $8.26*
Elgin | 112,400 | 38 | $8.17** | $5.87*
Geneva | 25,900 | 16 | $9.05 | $4.96
*served wholly/partially by various sanitary districts
** lime softening water treatment plant like West Chicago

## Slide 20: Rate Comparison
Chart: 
| Woodridge​ | Wheaton​ | Westmont​ | West Chicago​ | Villa Park​ | St. Charles​ | Montgomery​ | Lombard​ | Lisle​ | Glen Ellyn​ | Geneva​ | Elmhurst​ | Elgin​ | Downers Grove​ | Darien​ | Batavia​ | Aurora​ | Addison​
Sewer | 6.47 | 7.9 | 3.65 | 11 | 3.85 | 8.83 | 8.26 | 7.74 | 6.24 | 7.57 | 4.96 | 11.45 | 5.87 | 3.65 | 5.57 | 8.66 | 11.07 | 8.47
Water | 11.74 | 8.44 | 12.36 | 9.9 | 10.54 | 11.7 | 8.93 | 11.4 | 8.04 | 10.5 | 9.05 | 14.85 | 8.17 | 11.24 | 9.75 | 5.79 | 10.29 | 11.58

## Slide 21: Rate Comparison – Key Takeaways
Similar-sized communities aren't directly comparable
West Chicago is the only DuPage County community with a centralized Water Treatment Plant and a Wastewater Treatment Plant
Most DuPage County communities are served by DuPage Water Commission
    (No Active Wells or WTP)
Many are served by separate Sanitary Districts
    (independent taxing bodies-cost on property tax bill)
Rates should be based on infrastructure maintained locally, not population
A water/sewer rate study is underway

## Slide 22: Pre-planned Rate Schedule
Ordinance No. | Date Passed | Date Effective | Water Rate | Sewer (Residential) | Sewer (Commercial)
23-O-0025 | 9/5/23 | 1/1/26 | $9.90 | $11.00 | $11.34
 | 9/5/23 | 1/1/27 | $10.40 | $11.50 | $11.86
 | 9/5/23 | 1/1/28 | $11.00 | $12.15 | $12.53
Average Bi-Monthly Residential Water & Sewer Bill (15,000 gallons usage, ¾" meter) |  |  |  | 
 | 2025 | 2026 | 2027 | 2028
Water | $148.21 | $153.84 | $160.09 | $167.60
Sewer | $161.50 | $169.00 | $176.50 | $186.25
Total | $309.71 | $322.84 | $336.59 | $353.85

## Slide 23: Status of the Rate Study & Staff Recommendation
Contract executed on May 18, 2026
Project kickoff meeting held on June 18, 2026
Interactive meetings held on August 12 and October 8 – Reviewed current infrastructure water and sewer systems; current and proposed 5-year CIP; inflation assumptions; funding alternatives; financial modeling and long-term planning including but not limited to water meter replacement, emergency connections, declining demand, watermain replacement program, wastewater treatment, lift station consolidation, etc.
Expected to be completed in Early 2027.
Staff recommendation is to continue with pre-planned rate increase in 2027.

## Slide 24: Questions?
Seeking Direction if Different than proposed